## Slide 1: Cross-Layer Design for Spectrum- and Energy-Efficient Wireless Networks
Guowang Miao
miao@FreeLinguist.com

## Slide 2: Presenter Introduction
Founder of FreeLinguist®, a cloud platform for you to connect with native linguists for quality language services, such as translation, editing, or writing services.
Expert in communications and networking
Well known for his original contributions in building a set of fundamental energy-efficient communications theories, which are widely accepted nowadays.
Inventor of energy-efficient scheduling and capacity-approaching transmission (United States Patent 7782829).
Author of the graduate textbook entitled Fundamentals of Mobile Data Networks (Cambridge University Press)
Author of the book entitled Energy and Spectrum Efficient Wireless Network Design (Cambridge University Press).
Fruitful inventor with many granted patents, some of which have been adopted as essential in 4G standards.

## Slide 3: Outline
Introduction
Wireless Channel Properties
Basic Concepts
Spectrum Efficient Design
Energy Efficient Design
Energy-Efficient Mobile Access Networks: A Tradeoff Perspective
Conclusions and References

## Slide 4: 1. Introduction

## Slide 5: Ancient Wireless Communications
Invasion or no invasion? (1/0)
Wireless Communications at 400–790 THz (visible light)
Energy of firewood:16.2 megajoules/kg
Extremely spectrum and energy inefficient
Yet NEEDED
Notes: 5

## Slide 6: Growing Need of Energy-Efficient Design in Mobile Broadband Access Networks
Currently, 2% of world energy consumption due to mobile communications
  Radio access network consumes 80% energy of the mobile communications (Ericsson)
Mobile data traffic is exploding
  AT&T mobile data traffic increases by 80x
  after 2007 (Iphone debut).
  Cisco expects 26x further data traffic in 2015.
  Extrapolating Cisco traffic prediction curve,
  300x data traffic in 2020.

## Slide 7: Growing Need of Energy-Efficient Design in Mobile Broadband Access Networks
Price paid for this enormous growth
  Doubling of the power consumption in cellular networks (base stations and core network) every 4-5 years.
Energy consumption has dramatic environmental impact
  Vodafone: total annual emission of CO2 in 2007/8: 1.45 million tonnes
  More expected in the future

## Slide 8: Need of Energy Efficiency in Mobile Devices
Mobile devices are usually battery powered
Growing demand
of mobile traffic
Exponential growth
of battery consumption
(150% every two years)
Slow development
of battery
(10% every two years)
an exponentially increasing gap
between the energy demand and supply

## Slide 9
Slow advance in battery technology /energy industry critically limit energy availability
Significance of
energy efficiency
Growing demand for ubiquitous wideband wireless applications
Spectrum is a natural resource that cannot be replenished
Significance of
spectral efficiency
Affected by all layers of system design
Cross-layer optimization to exploit interactions between different
layers to fully improve both spectral and energy efficiency
Critical Demand of SE and EE

## Slide 10: Motivation for Cross-Layer Design
Traditional Open System Interconnection (OSI) model
  Divide communication systems into layers
Cons of separate design
  Information lost between layers
Necessity of cross-layer design, especially for wireless communications

## Slide 11: Revolutionary Thinking Needed
Radio Resource Management of wireless networks
allocate radio resources
modulation
/coding
power
Cell deployment
T/F/S/C-domain
channel allocation
statically
dynamically
data rate
…
assurance of quality of service (QoS)
for mobile users (rate, delay, outage, coverage, etc.)
Energy IGNORED!

## Slide 12: Revolutionary Thinking Needed
Radio Resource Management of wireless networks
allocate radio resources
modulation
/coding
power
Cell deployment
T/F/S/C-domain
channel allocation
statically
dynamically
data rate
…
assurance of quality of service (QoS)
for mobile users (rate, delay, outage, coverage, etc.)

## Slide 13: 2. Wireless Channel Properties

## Slide 14: Propagation and Mobility
Propagation
  Fading, shadowing
  Reflection at large obstacles, refraction, scattering at small obstacles, diffraction at edges
  Signal takes several paths to the receiver
Mobility
  Variation of channel characteristics
signal at sender
signal at receiver
LOS pulses
multipath
pulses

## Slide 15: Fundamental Problem I
signals at sender
signal at receiver
LOS pulses
multipath
pulses
HOW to exploit wireless channel
properties to enhance both spectral
and energy efficiency for single-link
communications ?

## Slide 16: Multiple User Perspective
Wireless channels
  Broadcast of all signals
  Due to frequency reuse, different users affect each other through
    Interference
Forms of Interference

## Slide 17: Fundamental Problem II
HOW to exploit interference
properties to enhance both spectral
and energy efficiency for
the whole network ?

## Slide 18: 3. BASIC CONCEPTS

## Slide 19: Physical Layer
Physical (PHY) layer
  Deal with challenging wireless medium
  Traditionally
    Operate on a fixed set of operating points
      Fixed transmit power
      Fixed modulation and coding scheme (MCS)
    Pro:
      Simplicity
    Con:
      Channel capacity not fully exploited (low SE)
      Excessive energy consumption (low EE )
  Link adaptation: adapt to QoS and environments

## Slide 20: Multi-User Perspective
Typically more than one user in the network
Multiple users need to share wireless medium
Medium access control: share wireless channel efficiently
  allocate wireless resources to users on demand
  multiplex/separate transmissions of different users
  avoid interference and collisions
  network-wide flexibility, efficiency, and fairness of resource sharing

## Slide 21: Wireless Resources
Orthogonal resources in four dimensions
  Space ( s )
  Time ( t )
  Frequency ( f )
  Code ( c )

## Slide 22: Wireless Resources
Non-orthogonal resources
  Power
    Users with completely different ( s, t, f, c )
      Independent communications
    Two or more users with overlapping ( s, t, f, c )
      Interact with each other through mutual interference
        Controlled by power
      Examples:
        Inter-cell interference in cellular networks (s overlap)
        Inter-symbol interference (t overlap)
        Inter-channel interference (f overlap)
    Energy consumption
B
C
A
D

## Slide 23: MAC Classification
MAC determines resource allocation
  Centralized and distributed MAC
Centralized MAC
  Central controller schedules resources of all users
  Examples: data channels in cellular networks
  Pros: high performance, easy control of resource assignments …
  Cons: high complexity, poor scalability …

## Slide 24: Distributed MAC
Distributed MAC
  No central scheduler
  Individual users decide resources independently
    Use a certain local medium access policy
  Examples: Aloha, CSMA/CA, 802.11 DCF
  Low-complexity, high scalability
  Protocol design determines how network performs

## Slide 25: Design Rules of Distributed MAC
Traditional rules of distributed MAC design
  Removal of Idle State
    Some users have data to transmit but decide not to while channel is idle
    Waste of channel capacity
    Happen frequently with light network load
  Removal of Collision State
    With collision, packet transmission fails
    Waste of both channel capacity and user energy
    Happen frequently with high network load

## Slide 26
Exploit wireless medium properties
  Optimize point to point communication links
  Allocate resources to share wireless medium fairly and efficiently
Enhance spectral and energy efficiency through joint optimization of
  Physical layer: power control, adaptive modulation and coding, etc., i.e. link adaptation
  Medium access control (MAC) layer: control the medium access in a distributed or centralized way
based on knowledge of channel state information.
CSI can be obtained through reciprocity in TDD systems or independent feedback channels.
Focus
Time
User 1
SNR
User 2
User 3
Notes: Font problem

## Slide 27: 4. Cross-Layer Optimization for Spectral Efficiency

## Slide 28: Multiuser Diversity in A Single Channel System
Exploit channel property
  Schedule the user with good channel quality
Techniques required to exploit multiuser diversity:
  Channel state information feedback
  Adaptive modulation and coding
  Fast channel-aware packet scheduling
Diversity gain increases with the number of users
Time
User 1
SNR
User 2
User 3

## Slide 29: System Model
l1
Q1(t) r1(t)
l2
Q2(t) r2(t)
lM
QM(t) rM(t)
OFDM
DSA or/and APA
Queue Information
Channel Information
User 1
User 2
User M
Rate Adaptation (RA)
Dynamic Subcarrier assignment (DSA)
Adaptive Power Allocation (APA)
f
SNR
2(f)
1(f)
User 1
User 2
f
Power

## Slide 30: Cross-Layer Optimization Based on Utility Functions
Utility: the level of satisfaction that a user gets from using some resources (economics concept)
Utility functions are determined by applications
Optimization
  Objective: to maximize the sum of utilities in the system
  Subject to: the degrees of freedom of resource allocation
    DSA: Orthogonality of subcarriers
    APA: Maximum total transmit power
  Pros:
    Application-oriented resource allocation
    Flexibility
    Fairness & QoS provisioning
Utility
Rate
Utility
Rate
Delay
Utility
Voice
Best-effort
Time-sensitive

## Slide 31: Scope
Objective: To maximize
the total utility
Utility functions w. r. t. average delays
Utility functions w. r. t. instantaneous data rates
Utility functions w. r. t. average data rates
Best-effort traffic
DSA and APA
optimization
algorithms
Fairness
Stability
QoS differentiation for heterogeneous traffic
Utility functions w. r. t. data rates
Channel-aware
scheduling
Channel- and queue-aware
scheduling
Time-sensitive traffic
w.r.t. : with respect to

## Slide 32: Scope
Objective: To maximize
the total utility
Utility functions w. r. t. average delays
Utility functions w. r. t. instantaneous data rates
Utility functions w. r. t. average data rates
Best-effort traffic
DSA and APA
optimization
algorithms
Fairness
Stability
Utility functions w. r. t. data rates
Channel-aware
scheduling
Channel- and queue-aware
scheduling
Time-sensitive traffic
w.r.t. : with respect to

## Slide 33: Utility-Based Dynamic Subcarrier Assignment
Sorting-Search Algorithm for DSA
  Complexity is about M2Klog2(K)
  Nearly optimal
Nonlinear combinatorial optimization problem with computational complexity MK.
  M: the number of users
  K: the number of subcarriers
r2
r1

## Slide 34: Utility-Based Adaptive Power Allocation
Multi-level water-filling

## Slide 35: Simulation Results
5 dB
10 dB

## Slide 36: Scope of Research
Objective: To maximize
the total utility
Utility functions w. r. t. average delays
Utility functions w. r. t. instantaneous data rates
Utility functions w. r. t. average data rates
Best-effort traffic
DSA and APA
optimization
algorithms
Fairness
Stability
Utility functions w. r. t. data rates
Channel-aware
scheduling
Channel- and queue-aware
scheduling
Time-sensitive traffic
w.r.t. : with respect to

## Slide 37: Channel-Aware Scheduling Using Rate-Based Utility Functions
Users care about the average data rate during 1 to 2 seconds, not the instantaneous one.
  Average data rate:
  Optimization objective:
The solution for DSA is very simple.
A utility function is associated with a kind of fairness
Multichannel proportional fair scheduling
Priority
Achievable instantaneous rate

## Slide 38: Scope of Research
Objective: To maximize
the total utility
Utility functions w. r. t. average delays
Utility functions w. r. t. instantaneous data rates
Utility functions w. r. t. average data rates
Best-effort traffic
DSA and APA
optimization
algorithms
Fairness
Stability
QoS differentiation for heterogeneous traffic
Utility functions w. r. t. data rates
Channel-aware
scheduling
Channel- and queue-aware
scheduling
Time-sensitive traffic
w.r.t. : with respect to

## Slide 39: Max-Delay-Utility (MDU) Scheduling
Utility functions w.r.t. average waiting time
  Average waiting time, W  Satisfaction level, U(W)
Optimization problem of MDU scheduling
  Objective: to maximize the total utility with respect to the predicted average waiting time at each time slot
Joint channel- and queue-aware scheduling
  Awareness of channel conditions  improve network capacity
  Awareness of queue information  ensure QoS

## Slide 40: Stability Region
Ergodic capacity region vs. Stability region
  Ergodic capacity region consists of all (long-term) average data rate vectors under all possible resource allocation schemes, given the statistics of the channels
  Stability region of a scheduling policy is defined to be the set of all possible arrival rate vectors for which the system is stable under the policy.
  Stability region  Ergodic capacity region
  Maximum stability region: the largest stability region that can be achieved by some scheduling schemes ( Ergodic capacity region)
  MDU has maximum stability region.
0
λ1
λ2
r1
r2
0
AMC, No DSA
AMC, DSA
No AMC, No DSA

## Slide 41: Recap
Centralized Cross-Layer Optimization for SE
Intelligent resource allocation by exploiting channel and queue information
  Efficient resource allocation algorithms
Diverse QoS provisioning offered by utility functions
Significant performance gains: multiuser diversity, frequency diversity, and time diversity

## Slide 42: Distributed MAC - Traditional Slotted Aloha
Time divided into slots of equal size
Users wait until beginning of slot to transmit
If collision: retransmit with probability p until success.

## Slide 43: Access Modeling
Control the
contention probability
Fading on one
subchannel
Cons of separate design: 1. transmit a frame when channel is in deep fading; 2. May not transmit but channel is in good condition
With cross-layer design
  Transmit a frame when channel gain is above a threshold
  Randomize transmission since channel varies randomly
Find optimal values
to max network
performance

## Slide 44: Opportunistic Random Access – Infrastructure Networks
Exploits variation inherent in wireless channels to increase network throughput.
Each user knows its own channel state
[Qin 03] Each user transmits only if its channel power gain is above a pre-determined threshold that is chosen to maximize the probability of successful transmissions.

## Slide 45: Channel-Aware Aloha
N users in the system to send data
Each user knows the distribution of its channel gain
Each user chooses a threshold Ho and sends data only if the channel gain is above Ho (binary scheduling).
Contention probability: 1/N
Asymptotically optimal in N
Asymptotically achieve 1/e of the
centralized system’s throughput
[YU06]: binary scheduling maximizes
the sum-throughput

## Slide 46: Opportunistic Random Access – Ad Hoc Networks
Ubiquitous communications complicate network topology
No central scheduler for good scalability
A generic solution
0.1
10.1
1.8
1.3
0.3
0.9
2.6
26.1
16.1
Channel gain

## Slide 47: Cross-Layer Design Objective
Objective:
  Consider both overall network throughput and fairness
  Find optimal threshold configuration and adaptive modulation and coding (AMC)
Cross-layer design criterion
Notes: Itemize constraint

## Slide 48: Decentralized Optimization for Multichannel Random Access (DOMRA)
Original problem: difficult to globally optimize
Objective function is equivalent to:
    reduce transmission collisions of the whole network.
    maximize the achieved data rate of each BS with transmission capability limit.
Problem decomposition:
  Subproblem 1: find optimal thresholds
    Resolves network collision
    Achieve proportional fairness
  Subproblem 2: find optimal power allocation policy
    Optimize individual transmission performance
    Satisfy average and instantaneous power constraints

## Slide 49: Optimal DOMRA - MAC Layer
Local knowledge:
    |Ti| : number of users receiving packets from User i
    |Ri|: number of users sending packets to User i
  Two-hop knowledge (typical in routing discovery):
  : total number of users sending packets to the interfering neighbors of User i
Optimal predetermined threshold
Neighborhood Information

## Slide 50: Threshold Adaptation
Low threshold
Very high
threshold

## Slide 51: Link Adaptation
  Capability-limited water-filling power allocation
Due to peak
power constraint
Due to average
power constraint

## Slide 52: Sub-Optimality Gap
Gap to the global optimum.
  Obtain feasible decentralized policy
  through subproblem decomposition
  Global optimum
    Global network knowledge
    Difficult to solve
    Exhaustive search

## Slide 53: Cochannel Interference Avoidance MAC (CIA-MAC)
Co-Channel Interference (CCI): the major factor limiting system capacity
CIA-MAC: improve downlink QoS of cell-edge users
Severe interferers: dominant interfering BSs; randomize transmission
Optimized by: DOMRA
  Threshold design to control BS random transmission

## Slide 54: How to Decide Severe Interferer?
Severe Interference: no MAC frame recovered after CRC due to CCI
  Interference to Carrier Ratio (ICR) of Interferer i:
  Severe Interferer Judgment
    Interferer i is a severe interferer when
    where is named CIA-MAC trigger.
  Transmission of severe interferer will always cause failure of packet reception in the MAC layer.
CIA-MAC is triggered when it achieves better network throughput
E(|Hi|2Pi)
ICRi=
E(|H|2P)

## Slide 55: Performance Improvement
CIA-MAC wins because: 1. full frequency reuse;
2. intelligent recognition of severe interferers.

## Slide 56: Existing Random Access Schemes
Channel-Aware Aloha, DOMRA: Aloha based, collision of entire data frames result in low channel utilization
Design signaling negotiation to avoid collision
Existing schemes (e.g. CSMA-CA):
  Backoff when collision without considering CSI
  Drawback: deferring transmission may result in data communications in deep fades.
Time
User 1
SNR
User 2
User 3
First try of U2 and U3, a collision
t1
t2
t3
U3 first counts down to 0 at t2 , transmits, but in a deep fade

## Slide 57: Infrastructure Networks[Qin04]
Opportunistic Splitting Algorithms
  Distributed splitting algorithm to reduce this contention.
  Resolve a collision and find the user with the best channel gain

## Slide 58: Opportunistic Splitting Algorithms [Qin04]
In the beginning of each mini-slot, users with Hl <h< Hh will transmit
At the end of each mini-slot, BS feeds back (0, 1, e) to all users
  0: idle
  1: success
  e: collision
Users update the two thresholds, Hl and Hh , and continue contention in the following mini-slots.
  Updates to minimize the collision probability in the following mini-slots
  Example: e: increase Hl to reduce the number of users in the range
Finally only one user is expected to have gain Hl <h< Hh .

## Slide 59: Ad Hoc Networks
0.1
10.1
1.8
1.3
0.3
0.9
2.6
26.1
16.1
Channel gain
Can distributed random access algorithms achieve
the performance of centralized algorithms?
How to do it?

## Slide 60: Channel Aware Distributed MAC (CAD-MAC)
60
Different traffic flows contend for channel access
  Senders determine channel access
  Two types of contentions
Type-I contention
  Links with the same transmitter
  Central scheduling
    (2,4), (2,8), and (2,10)
Type-II contention (focus)
  Among all other links
  Distributed random access
    (2,4) and (3,10)

## Slide 61: Resolution of Type-I Contention
Different channels experience gains of different distributions
Self-max-SNR scheduler
Distribution of corresponding
channel gain
channel gain
All links are scheduled with equal probability (fairness assurance)
Always schedule the link with the best instantaneous channel condition
relative to its own channel condition (performance assurance)
3. Same as max-SNR scheduler when all links are with i.i.d. channel distribution
E.g.: Rayleigh fading

## Slide 62: Resolution of Type-II Contention
1. Resolve contention in each CRS through a multi-stage channel-aware Aloha (similar to DOMRA, use threshold to control contention performance and fairness)
2. After one CRS, links with higher gains selected in a distributed way to continue the contention in the following CRS (through distributed threshold control )
3. Only one link with the best channel gain wins within each local area for data transmission, all neighbors informed to keep silent
Users selected in Type-I contention resolution are involved.

## Slide 63: Three-Step Signal Exchange

## Slide 64: Complete Contention Resolution
  CAD-MAC comparable to centralized schedulers
Theorem 1: With probability one, the contention
of any networks can be completely resolved by
CAD-MAC if sufficient CRSs are allowed.
Definition: The contention in a network is
Completely resolved if
all links that have won the contention can
transmit without collision;
2. if any additional link that has not won the
contention transmits, it will collide with at
least one link that has won the contention.

## Slide 65: Efficiency
Performance loss compared to a centralized scheduler
  Due to CRSs used to resolve the contention
  Define the efficiency of CAD-MAC to be:
  : average number of CRSs resolving contention
  Tc : CRS length; Tf : frame length

## Slide 66: Necessary CRSs
Theorem 2: For a network with N links, each interfering with all others,
where
Furthermore,
A special case:

## Slide 67: Necessary CRSs
Theorem 3: For a network of any type and size,
: transmission coexistence factor, the average number of links that win the contention in one frame slot
: contention coexistence factor, the average number of simultaneous resolutions in each CRS
Examples: two cellular networks that coexist

## Slide 68: Efficiency of CAD-MAC
CRS length Tc: round-trip time of signal propagation
Frame length Tf : channel coherence time
Example:
Cellular networks of 6km radius
round trip time: 50 [Leung 2002]
channel coherence time: tens of milliseconds with 900 MHz carrier frequency and user speed 72 km/h [Kumar 2008]
Efficiency close to unity.
Proposition 1: The efficiency of CAD-MAC satisfies,
For a network where each user interferer with all others,

## Slide 69: Robustness of CAD-MAC
What if users have imperfect CSI because of non-ideal channel estimation?
  Control medium access based on and
rather than the actual and
Theorem 3: Theorems 1, 2, and 3 and Proposition 1 hold
when all users have imperfect channel knowledge and
CAD-MAC is robust to any channel uncertainty.

## Slide 70: Simulation Performance – CRSs Needed for Complete Contention Resolution

## Slide 71: Simulation Performance

## Slide 72: 5. CROSS-LAYER OPTIMIZATION FOR ENERGY EFFICIENCY

## Slide 73: Energy Saving Energy Efficiency
Complete Saving of Energy
  Shut down network completely to save the most energy
  Not desired!
Purpose of energy-efficient wireless network design
  Not to save energy
  Make the best/efficient use of energy!
Energy saving
w/o
losing service quality

## Slide 74: Energy and Communications
Essence of communications
  Use energy to move information from sender to receiver
What is energy?
The ability to move things

## Slide 75: Transmit Power Concern
Information theorists studied energy-efficient communications for at least two decades [Gallager88,Verdu90]
  Transceivers designed to maximize information bits per unit energy
  Use infinite degrees of freedom per bit, e.g. infinite bandwidth or time duration
    Example:
      Energy consumption per bit in AWGN channels:
      Minimized when t or W is infinite
        Emin = No ln 2 / g

## Slide 76: Energy Consumption Per Bit
Uncoded MQAM
Optimal Coding
[Prabhakar01]

## Slide 77: Lazy Packet Scheduling [Prabhakar01]
Minimize energy to transmit packets within a given amount of time.
Packet arrival time ti.
All packets are of the same size.
Question: what’s the transmission duration for each packet so that the total energy transmitting all the packets is minimized?

## Slide 78: Optimal Offline Scheduling
Intervals between two pckts
Transmission time for each packet
Answer: divide available transmission time evenly among all packets and extend the transmission time as long as possible
Optimal online scheduling: exploit this property while considering
current buffer size
future arrivals (statistics of arrival process)
time left

## Slide 79: Energy Consumption in Practice
RF transmit power:
  Consumed by PA for reliable delivery of data
Circuit component power:
  Consumed by electronic circuits for reliable device operations

## Slide 80: A Detailed Analysis of Energy Consumption
[Li, Bakkaloglu, and Chakrabarti, 07]

## Slide 81: Our Interest: Wireless Solution
Transmit mode critical for power consumption
  Radio interfaces account for more than 50% of overall system energy budget for a smart cellular phone [Anand2007].
  Selection is critical
Our focus: transmit mode
Emphasize PHY and MAC to improve energy efficiency in transmit states
Power consumption of 802.11 transceivers[Man05]

## Slide 82: Another Look at the Issues
Circuit power Pc
  Used by all other electronics (filters, AD/DA)
  Device dependent
  A fixed energy cost in transmit mode
Transmit power PT(R)
  Used by power amplifier for reliable
  bit transmission
  Power for reliable transmission of R
  Depend on modulation, coding and channel
  Selection of R determines energy efficiency
Need to balance conflicting design guidelines to optimize
  Transmit energy: Extend transmission time as long as possible [Meshkati06], [Prabhakar01]
  Circuit energy: Use highest rate supported and finish transmission ASAP
How to optimize the balance between transmit & circuit energy?
Across all subchannels?

## Slide 83: Energy-Efficient OFDM and MIMO
Approach
  Allocate power, adapt modulation and coding based on channel state information to
    reduce power consumption of point to point links;
    and balance the competing behaviors of multicell energy-efficient communications
F1
F1
F1
F1
F1
F1
F1
OFDM and MIMO:
  Key technologies in next-generation wireless communications
  Few work done for energy-efficient OFDM and MIMO

## Slide 84: Energy Efficiency Metric
Send as much data as possible given a certain amount of energy
Given any small amount of energy consumed in a transmission duration of , send a maximum amount of transmitted data
Choose the optimal link adaptation, i.e. power and MCS (modulation and coding scheme), to maximize
which is equivalent to maximize
called energy efficiency with a unit bits per Joule.
Different from existing throughput maximization schemes: variation of overall transmit power
Overall data rate on all subchannels
Vector, data rates on all subchannels

## Slide 85: Energy Efficiency in Flat Fading Channel

## Slide 86: Optimal Energy Efficient Link Adaptation in Flat Fading Channels
Optimal energy efficient transmission rule [Miao07]
  Mobile users always operate with optimal modulation mode
  with optimal energy-efficient link adaptation
Energy Consumption to transmit 1 Mb of data
Optimal

## Slide 87: Properties of Energy-Efficient Link Adaptation
  To improve energy efficiency, we should
    Increase channel gain
    Reduce circuit power
    Increase the number of subchannels
  The data rate, determined by link adaptation, should
    Increase with channel gain
    Increase with circuit power
    Decrease with the number of subchannels
[Miao, TCom10]: Relationship of energy efficiency, distance, and rate

## Slide 88: Upper Bound
Upper bound of energy efficiency
With Shannon capacity, it is g/(No ln2) .
How to achieve it?
  1. Zero circuit power and transmit with infinite small data rate
  2. Infinite number of subchannels and transmit with infinite small data rate.

## Slide 89: Conditions for Global Optimum
Concept of Quasiconcavity:
A local maximum is also a global maximum
x1
x2

## Slide 90: Optimal Energy-Efficient Transmission
Energy efficiency
  strictly quasiconcave
A unique global optimal link adaptation exists and is characterized by
Measure how good a subchanel is

## Slide 91: Optimal Energy-Efficient Transmission
Example: Shannon capacity achieved on each subchannel:
dynamic water-filling
Classical water-filling
where is determined
by the peak power limit
Optimally balance circuit energy consumption and transmit energy consumption on all OFDM subchannels

## Slide 92: Energy-Efficient Downlink Transmission
A generic EE transmission theory
  Find PT(R)
Example: BS downlink OFDMA transmission [Xiong11]
  A special case of wireless transmission
  Except: before transmission, the BS needs to assign the subcarriers to users according to certain rules.
  After scheduling: the base station needs to determine transmission modes

## Slide 93: Algorithm Development-Frequency Selective Channels
Binary search assisted ascent (BSAA) for link adaptation in frequency-selective channels
A type of concave fractional programs
  Many standard methods for concave programs can be used
  E.g. Dinkelbach’s algorithm (converges superlinearly)
  Details in [Isheden 2011]

## Slide 94: Convergence of BSAA
Improvement of energy efficiency with iterations.
PDF of # of iterations for convergence

## Slide 95: Performance Comparison
Energy-efficient link adaptation always achieves the highest energy efficiency
A tradeoff between energy efficiency and spectral efficiency exists
15dBm
20dBm
25dBm

## Slide 96: Energy Efficiency Metric
Exponentially weighted moving average low-pass filters
  Average throughput at time t
  Average power consumption at time t
Average energy efficiency metric:
circuit power
overall transmit power on all subchannels

## Slide 97: Low-Complexity Energy-Efficient Link Adaptation
Note
Dynamic water-filling power allocation to the level determined by the previous energy efficiency.
Water level determined by previous energy efficiency

## Slide 98: Multi-User Energy Aware Resource Allocation
Max arithmetic average of energy efficiency (w/o fairness)
Max geometric average of energy efficiency (w/ fairness)
  Energy aware resource allocation based on maximizing network “throughput per joule” metric
In a multi-user system, all subchannels cannot be assigned to one user
How to assign subchannels?

## Slide 99: Resource Allocation w/o Fairness
Allocation metric:
  For user n on subchannel k
  Assign subchannel k to the user with the highest metric
  Closed-form resource allocation w/o fairness
  Circuit power >> transmit power (short distance commun.) and circuit power the same for all users
Max-SINR scheduler

## Slide 100: Resource Allocation w/ Fairness
Allocation metric:
  For user n on subchannel k
  Assign subchannel k to the user with the highest metric
  Closed-form resource allocation w/ fairness
  Circuit power >> Transmit power (short distance commun.)
Traditional Proportional
Fair scheduler

## Slide 101: Performance—Link Adaptation

## Slide 102: Interference-Aware Energy Efficient Communication
What will happen in a multi-cell interference-limited scenario?
For example: cell-edge users in cellular network environment.

## Slide 103: Two-User Cooperation
Consider two-user case to obtain insight
  Users 1 and 2 cooperates to determine their transmit powers
  Both have complete network knowledge
Problem modeling
Generally:
  Non concave
  Intractable

## Slide 104: Cooperative Power Optimization for Special Regimes
  Transmitter condition:
  1. circuit power >> transmit power
  2. transmit power >> circuit power
  Receiver condition:
  1. noise power >> interference
  2. interference >> noise

## Slide 105: Circuit Power Dominated Regime
When circuit power dominates power consumption
  Equivalent to throughput optimization
  Binary power control [Anders 06]
Power of User 2
Power of User 1
Sum energy efficiency
User 1 transmit max pwr and User 2 is shut down

## Slide 106: Transmit Power Dominated Regime
When the circuit power is negligible
Users transmit with the lowest power and MCS for maximum energy efficiency [Meshkati06]
Low Power
High Power
Low Power
High Power

## Slide 107: Noise Dominated Regime
When noise power dominates interference plus noise power
Interference treated as noise
Independent energy-efficient link adaptation

## Slide 108: Interference Dominated Regime
Interference far larger than noise power
On-Off energy-efficient power control, e.g. time sharing, is optimal
Access protocol design is important
  Orthogonalize signals of different users
  SE protocols are also EE
    DOMRA, CIA-MAC, CAD-MAC
Link adaptation is different from
those for SE optimization
Energy-efficient power setting

## Slide 109: Intractability for General Cases
What’s the situation for normal regimes?
  Non-concavity
  Multiple local maximums
  Behaviors of local maximums hard to predict
Multiple subchannels and users further complicate the problem
Impractical — complete network knowledge
What can we do?
Non-cooperative

## Slide 110: Non-Cooperative Energy-Efficient Power Optimization
User n chooses power to selfishly optimize energy efficiency
  Note: not appropriate for throughput, i.e. SE, maximization
    1). Aggressive power control: selfish users increase transmit power beyond what is reasonable [Goodman 2000]
    2). Pricing is needed to regulate the aggressive behaviors [Gesbert2007]
Observation:
  A variation of traditional spectral-efficient power control with power pricing
  Socially favorable
SE optimal
Power pricing
Non-cooperative energy-efficient power control is desirable to reduce interference and improve throughput in a non-cooperative setting.

## Slide 111: Properties of Equilibrium
Equilibrium:
  The condition that competing influences are balanced
  Its properties are important to network performance
We analytically show:
  The equilibrium always exist;
  Necessary and sufficient conditions of the equilibrium
  With flat fading channels, the equilibrium is unique, regardless of network conditions (channel gains, user distribution)
  With frequency-selective channels, the number of equilibrium depends on interference channel gains

## Slide 112: Equilibrium in Frequency-Selective Channels
In frequency-selective channels,
  An example with at least two equilibria
    One equilibrium:
    Another due to symmetry of network assumptions
Notes: Jacobian matrix

## Slide 113: Equilibrium in Frequency-Selective Channels
Sufficient conditions to assure a unique equilibrium
where ||A|| is the Frobenius norm of A.
  Not necessary: flat-fading channel cases
only depend on
interference channel gains
independent of
interference channel gains

## Slide 114: Equilibrium Power
Define Network coupling factor
Characterizes what level different transmissions interfere with each other
Eqiulibrium power adapts to interference strength: stronger intf., lower pwr

## Slide 115: Performance in a 7-Cell Cellular Network
EE scheme
EE scheme
SE scheme
SE scheme

## Slide 116: 6. Energy-Efficient Mobile Access Networks: A Tradeoff Perspective
116

## Slide 117
Key Design Constraints
Tombaz, A. Västberg and J. Zander, Energy and Cost Efficient Ultra High Capacity Wireless Access", IEEE Wireless Communication Magazine, vol. 18, no. 5, pp. 18- 24, October 2011.

## Slide 118: Tradeoffs in Cellular Network Design

## Slide 119: DE – EE
DE: a measure of system throughput per unit of deployment cost
  An important network performance indicator for mobile operators.
DE consists of
  Capital expenditure (CapEx)
    Infrastructure costs (base station equipment, backhaul transmission equipment, site installation, and radio network controller equipment.)
  Operational expenditure (OpEx)
    electricity bill, site and backhaul lease, and operation and maintenance cost

## Slide 120: Conflicting Design Rules
DE:
  Large cell radius to save expenditure on site rental, base station equipment, and maintenance, etc.
EE:
  Smaller cell radius to save transmit power
  Example [Badic 2009]:
    By shrinking the cell radius from 1, 000 m to
    250 m, the maximum EE of the HSDPA Network
    will be increased from 0.11 Mbits/Joule to 1.92
    Mbits/Joule, respectively

## Slide 121: Some Practical Considerations
Previous DE-EE tradeoff assumes
  deployment cost scales continuously and proportionally with the cell radius.
  only transmit power
In reality
  the equipment cost does not scale proportionally with the target cell size;
  the total network energy includes both transmit-dependent energy (e.g. power consumed by radio amplifier) and transmit-independent one (e.g. site cooling power consumption).
The relation of DE and EE may deviate from the simple tradeoff curve and become more complex when considering practical aspect

## Slide 122: Area Power Consumption and BS Density
Tombaz, A. Västberg and J. Zander, Energy and Cost Efficient Ultra High Capacity Wireless Access", IEEE Wireless Communication Magazine, vol. 18, no. 5, pp. 18- 24, October 2011.

## Slide 123: BW-PW
Converge to
Given a data transmission rate
  Expansion of signal bandwidth reduces transmit power and achieves better energy efficiency.

## Slide 124: BW-PW: In Practice
Given a data transmission rate
  Expansion of signal bandwidth reduces transmit power and achieves better energy efficiency.
In practice:
  the circuit power consumption, such as filter loss, actually increases with the system BW

## Slide 125: Circuit PW Scales with Bandwidth

## Slide 126: DL-PW
According to Shannon:
Power needed for reliable delivery of one bit
Time needed for sending one bit, i.e. delay

## Slide 127: DL-PW: In Practice
Other device power needed to enable operation:
127
Other device power

## Slide 128: DL-PW: One Step Further
Traffic dynamics
  Delay include both the waiting time in the traffic queue and the time for transmission
A(t)
m(P(t), H(t))
Avg. Power
Avg. Delay
Min. Avg. Energy Required for Stability
[Berry and Gallager 2002]
Open problem with practical considerations

## Slide 129: SE-EE
In single-user scenario
  SE
  EE
  SE-EE relationship

## Slide 130: SE-EE In Practice

## Slide 131: SE-EE: In Practice
Reduced tradeoff between energy efficiency and spectral efficiency w/ interference
Interference bounds SE
EE is sensitive to pwr, but SE is not .
EE schemes are advantageous in interference-limited scenarios
Tradeoff decreases with intf.

## Slide 132: 7. CONCLUSIONS AN REFERENCES
132

## Slide 133: Conclusion
Cross-layer optimization for SE
  Spectral-efficient link adaptation
  Spectral-efficient centralized MAC
  Spectral-efficient distributed MAC
Cross-layer optimization for EE
  Energy-efficient link adaptation
  Energy-efficient centralized MAC
  Energy-efficient distributed MAC
Energy-Efficient Mobile Access Networks: A Tradeoff Perspective

## Slide 134: Light Analogy
Oil lamp ( first mass produced)
(1G?)
Gas lights
(2G?)
Electrical lamps
(3G and beyond?)
Brighter and brighter …
(Higher and higher lumen capacity)
And ……

## Slide 135: Light Analogy
1780, oil lamp
1794, gas lamp
From 1800, electric lamp
1926, fluorescent lamp
(1/5 energy consumption, 5 years life)
1962, LED lamp (40% further energy reduction, 32 years life)
1973, compact fluorescent lamp
145 years capacity improvement …
87 years of energy efficiency enhancement!

## Slide 136: Implications ….
Where are we?
1G
2G
3G
4G
2.5G
Faster?
(how faster do we need)
Sustainable design
1980s, 28KBPS
1990s, 100KBPS
2000s, 2MBPS
2010s, 100MBPS

## Slide 137: More Information
Cambridge University Press

## Slide 138
REVOLUTIONAL
THINKING
AHEAD

## Slide 139: Acknowledgement
Dr. Guocong Song
provide slides related to utility-based centralized scheduling.

## Slide 140: References
S. Sampei, S. Komaki, S., and N. Morinaga, “Adaptive modulation/TDMA scheme for personal multimedia communication systems,” in Proc. Of 1994 IEEE Global Telecommun. Conf., Nov. 1994, pp. 989–993.
M. Ouchi, H. J. Lee, S. Komaki, and N. Morinaga, “Proposal for modulation level controlled radio system applied to atm networks,” in Proc. of Fourth European Conference on Radio Relay Systems, Oct. 1993, pp. 322–327.
G. Song and Y. (G.) Li, "Utility-based resource allocation and scheduling in OFDM-based wireless broadband networks,” IEEE Communications Magazine, Dec. 2005.
G. Song and Y. (G.) Li, "Cross-layer optimization for OFDM wireless networks - part I: Theoretical framework," IEEE Transactions on Wireless Communications, March 2005.
G. Song and Y. (G.) Li, "Cross-layer optimization for OFDM wireless networks - part II: Algorithm development," IEEE Transactions on Wireless Communications, March 2005.
G. Song and Y. (G.) Li, "Asymptotic throughput analysis for channel-aware scheduling,"IEEE Transactions on Communications, vol.54, no.10, pp.1827-1834, Oct 2006.

## Slide 141: References
G. Song, Y. (G.) Li, and L. J. Cimini, Jr. "Joint channel- and queue-aware scheduling for multiuser diversity in wireless multicarrier networks," IEEE Transactions on Communications, vol.57, no.7, pp. 2109-2121, July 2009.
G. W. Miao, N. Himayat, G. Y. Li, and A. Swami, “Cross-layer optimization for energy-efficient wireless communications: a survey,” Wireless Commun. and Mobile Computing, vol. 9, no.4, pp. 529-542, Apr. 2009.
X. Qin and R. Berry, “Exploiting multiuser diversity for medium access control in wireless networks,” in Proc. IEEE INFOCOM 2003, San Francisco, CA, Apr. 2003, pp. 1084-1094.
K. Bai and J. Zhang, “Opportunistic multichannel Aloha: distributed multiaccess control scheme for OFDMA wireless networks,” IEEE Trans. Veh. Tech., vol. 55 no. 3, pp. 848-855, Mar. 2006.
X. Qin and R. Berry, “Opportunistic splitting algorithms for wireless networks,” in Proc. IEEE INFOCOM 2004, Hong Kong, P.R. China, Apr. 2004, pp. 1662-1672.
G. Ganesan, G. Song, and Y. (G.) Li, “Asymptotic throughput analysis of distributed multichannel random access schemes,” in Proc. IEEE Conf. Commun. (ICC’ 2005), Seoul, South Korea, May 2005, pp. 3637-3641.
C. Y. Wong, R. S. Cheng, K. B. Letaief, and R. D. Murch, “Multiuser OFDM with adaptive subcarrier, bit, and power allocation," IEEE J. Select. Areas Commun., vol. 17, no. 10, pp. 1747-1758, Oct. 1999.

## Slide 142: References
Okada,T., Aikawa,S., 1992, "The Design of All Digital Multi-Level Modulator and Its Application to Variable Capacity Transmission", IEICE Trans. Japan, J75-B-11, 6, 325-336
S. Adireddy, and L. Tong, “Exploiting decentralized channel state information for random access,”IEEE Trans. Inf. Theory, vol 51, no. 2, pp. 537-561, Feb. 2005.
A. Maharshi, L. Tong, and A. Swami, “Cross-layer designs of multichannel reservation MAC under Rayleigh fading,” IEEE Trans. Signal Processing, vol 51, no. 8, pp. 2054-2067, Aug. 2003.
V. Naware, G. Mergen, and L. Tong, “Stability and delay of finiteuser slotted Aloha with multipacket reception,” IEEE Trans. Inf. Theory, vol 51, no. 7, pp. 2636-2656, July 2005.
G. W. Miao, G. Y. Li, and A. Swami, “Decentralized optimization for multichannel random access,” to appear in IEEE Trans. Commun., Oct. 2009.
Y. Yu and G. B. Giannakis, “Opportunistic medium access for wireless networking adapted to decentralized CSI,” IEEE Trans. Wireless Commun., vol. 5, no. 6, pp. 1445–1455, June 2006.
G. W. Miao, G. Y. Li, N. Himayat, and S. Talwar, “Cochannel interference avoidance MAC in wireless cellular networks,” IEEE Trans. Commun., vol. 57, no. 11, pp. 3397-3405, Nov. 2009.

## Slide 143: References
K. Lahiri, A. Raghunathan, S. Dey, and D. Panigrahi, “Battery-driven system design: A new frontier in low power design,” in Proc. Intl. Conf. on VLSI Design, Bangalore, India, pp. 261-267, Jan. 2002.
F. Meshkati, H. V. Poor, S. C. Schwartz, and N. B. Mandayam, “An energy-efficient approach to power control and receiver design in wireless networks,” IEEE Trans. Commun., vol. 5, no. 1, pp. 3306-3315, Nov. 2006.
S. Verdu, “Spectral efficiency in the wideband regime,” IEEE Trans. Inf. Theory., vol. 48, no. 6, pp. 1319–1343, June 2002.
G.W. Miao, N. Himayat, and G. Y. Li, “Energy-efficient link adaptation in frequency-selective channels,” IEEE Trans. Commun. vol. 58, no.2, pp. 545-554, Feb. 2010.
D. Goodman and N. Mandayam, “Power control for wireless data,” IEEE Pers. Commun. Mag., vol. 7, no. 2, pp. 48–54, Apr. 2000.
F. Meshkati, H. V. Poor, and S. C. Schwartz, “Energy-efficient resource allocation in wireless networks,” IEEE Commun. Magazine, pp. 58–68, May 2007.

## Slide 144: References
G. W. Miao, N. Himayat, G. Y. Li, A. T. Koc, and S. Talwar, “Interference-aware energy-efficient power optimization,” ICC 2009.
G. W. Miao, N. Himayat, G. Y. Li, and S. Talwar, “Distributed interference-aware energy-efficient power optimization,” IEEE Trans. on Wireless Commun., vol. 10, no. 4, pp. 1323-1333, Apr. 2011.
R. Mangharam, R. Rajkumar, S. Pollin, F. Catthoor, B. Bougard, L. Van der Perre, and I. Moeman, “Optimal fixed and scalable energy management for wireless networks,” in Proc. IEEE INFOCOM 2005, vol. 1, Mar. 2005, pp. 114–125.
P. Venkitasubramaniam, S. Adireddy, and L. Tong, “Opportunistic Aloha and Cross-layer Design for Sensor Networks,” Proc. of IEEE MILCOM, Oct. 2003, Boston, MA.
A. Y. Wang, S. Chao, C. G. Sodini, and A. P. Chandrakasan, “Energy efficient modulation and MAC for asymmetric RF microsensor system,” in Int. Symp. Low Power Electronics and Design, Huntington Beach, CA, 2001, pp. 106–111.
S. Cui, A. J. Goldsmith, and A. Bahai, “Energy-constrained modulation optimization,” IEEE Trans. Wireless Commun., vol. 4, no. 5, pp. 2349–2360, Sept. 2005.

## Slide 145: References
G. W. Miao, G. Y. Li, A. Swami, and N. Himayat, “Cross-layer optimization based on partial local knowledge,” in Proc. IEEE WCNC 2008, pp. 1513-1518, Mar. 2008.
G.W. Miao, N. Himayat, G. Y. Li, and D. Bormann, “Energy-efficient design in wireless OFDMA,” in Proc. IEEE ICC 2008, pp. 3307-3312, May 2008.
A. Anand, C. Manikopoulos, Q. Jones, and C. Borcea, “A quantitative analysis of power consumption for location-aware applications on smart phones,” in Proc. IEEE ISIE 2007, June 2007, pp. 1986–1991.
G. W. Miao, G. Y. Li, A. Swami, and N. Himayat, ``Channel aware distributed random access,’’ in Proc. IEEE Globecom 2009, Honolulu, HI, USA, Nov. 2009.
Jochen Schiller, Mobile Communications, 2nd edition, Addison Wesley, August 2003
William Stallings, Wireless Communications and Networks, 2nd edition, Prentice Hall, November 2004
  C. Isheden and G. P. Fettweis. 2011 (Mar.). Energy-Efficient Link Adaptation with Transmitter CSI. Pages 1381 – 1386 of: Proc. IEEE WCNC 2011.

## Slide 146: References
Y. Li, B. Bakkaloglu, and C. Chakrabarti, “A system-level energy model and energy-quality evaluation for integrated transceiver front ends,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 15, no. 1, pp. 90–103, Jan. 2007.
Y. Chen, S.-Q. Zhang, S.-G. Xu, and G. Y. Li, “Fundamental tradeoffs on green wireless networks,” to appear in IEEE Communications Magazine.
G. Y. Li, Z.-K. Xu, C. Xiong, C.-Y. Yang, S.-Q. Zhang, Y. Chen, and S.-G. Xu, “Energy-efficient wireless communications: tutorial, survey, and open issues,” to appear in IEEE Wireless Communications Magazine.
Theodore Rappaport, Wireless Communications: Principles and Practice, 2nd edition, Prentice Hall, December 2001
Andrea Goldsmith, Wireless Communications, Cambridge University Press, 2005
R. D. Yates, “A framework for uplink power control in cellular radio systems,” IEEE J. Sel. Areas Commun., pp. 1341–1347, Sep. 1995.
C. Xiong, G. Li, S. Zhang, Y. Chen, and S. Xu. 2011. Energy- and Spectral-Efficiency Tradeoff in Downlink OFDMA Networks. IEEE Trans.Wireless Commun., 10(11), 3874–3886.

## Slide 147: References
Y. Xue, T. Kaiser, and A. B. Gershman, “Channel-Aware Aloha-Based OFDM Subcarrier Assignment in Single-Cell Wireless Communications,” IEEE Trans. Commun., vol. 55, no. 5, pp. 953-962, May 2007.
G. W. Miao, N. Himayat, G. Y. Li, and S. Talwar, “Low-complexity energy-efficient scheduling for uplink OFDMA,” to appear in IEEE Trans. Commun.
A. Maharshi, L. Tong, and A. Swami, “Cross-layer designs of multichannel reservation MAC under Rayleigh fading,” IEEE Trans. Signal Processing, vol 51, no. 8, pp. 2054-2067, Aug. 2003.
A.J.Goldsmith and S. G. Chua “Variable-rate variable-power MQAM for fading channels,” IEEE Trans. Commun., vol. 45, no. 10, pp. 1218-1230, Oct. 1997.
A. GjendemsjÂ, D. Gesbert, G. E. Âien, and S. G. Kiani, “Optimal power allocation and scheduling for two-cell capacity maximization,” in Proc. RAWNET (WiOpt), Apr. 2006.
A. Gjendemsjo, G.E. Oien, and D. Gesbert, “Binary power control for multi-cell capacity maximization, ” SPAWC 2007.
S. Nanda, K. Balachandran, and S. Kumar, “Adaptation techniques in wireless packet data services,” IEEE Commun. Mag., vol. 38, no. 1, pp. 54–64, Jan. 2000.

## Slide 148: References
K. Kar, S. Sarkar, and L. Tassiulas, “Achieving proportional fairness using local information in Aloha networks,” IEEE Trans. Autom. Control, vol. 49, no. 10, pp. 1858-1863, Oct. 2004.
C. Schurgers, O. Aberthorne, and M. B. Srivastava, “Modulation scaling for energy aware communication systems,” International Symposium on Low Power Electronics and Design, pp. 96-99, 2001.
S. Cui, A. J. Goldsmith, an A. Bahai, “Energy-efficiency of MIMO and cooperative MIMO techniques in sensor networks,”IEEE JSAC, vol 22 no. 6, Aug. 2004.
J. F. Kiang, “Something You Should Know about Electromagnetic Applications,” online at http://cc.ee.ntu.edu.tw/~jfkiang/electromagnetic%20wave/electromagnetic%20applications(v1).pdf.
G. Y. Li, Z.-K. Xu, C. Xiong, C.-Y. Yang, S.-Q. Zhang, Y. Chen, and S.-G. Xu, “Energy-efficient wireless communications: tutorial, survey, and open issues,” to appear in IEEE Wireless Communications Magazine.
B. Badic, T. O’Farrel, P. Loskot, and J. He, “Energy efficiency radio access architectures for green radio: Large versus small cell size deployment,” in Proc. of IEEE 70th Vehicular Technology Conference (VTC Fall), Anchorage, USA, Sept 2009.
W. Yu and J. M. Cioffi, “FDMA capacity of Gaussian multiple-access channels with ISI,” IEEE Trans. Commun., vol. 50, no. 1, pp. 102–111, Jan. 2002.

## Slide 149: References
K. Lahiri, et. al., “Battery-Driven System Design: A New Frontier in Low Power Design”
R. G. Gallager, Information Theory and Reliable Communication. John Wiley & Sons, Inc., 1968.
B. Badic, T. O’Farrel, P. Loskot, and J. He, “Energy efficiency radio access architectures for green radio: Large versus small cell size deployment,” in Proc. of IEEE 70th Vehicular Technology Conference (VTC Fall), Anchorage, USA, Sept 2009.
Y. Chen, S. Zhang, and S. Xu, “Characterizing energy efficiency and deployment efficiency relations for green architecture design,” in Proc. of IEEE International Communications Conference (ICC), Cape Town, South Africa, May 2010.
R. Berry and R. Gallager. Communication over fading channels with delay constraints. IEEE Transactions on Information Theory, vol. 48, no. 5, pp. 1135-1149, May 2002.
C. Zeng, L. M. C. Hoo, and J. M. Cioffi, “Efficient water-filling algorithms for a Gaussian multiaccess channel with ISI,” in Proc. IEEE Vehicular Technology Conf., 2000, pp. 1072–1077
Tombaz, A. Västberg and J. Zander, Energy and Cost Efficient Ultra High Capacity Wireless Access", IEEE Wireless Communication Magazine, vol. 18, no. 5, pp. 18- 24, October 2011.
Numerous slides and other resources publicly available on the Internet

## Slide 150
Q&A